## Slide 1
+X
-X
+Y
-Y
+X
-X
+Y
-Y
Left Stick
Right Stick
RIGHT
LEFT
UP
DOWN
DPAD
Y
B
A
X
Instructions for Robot Platform Driver
Right Trigger
Right Bumper
Left Trigger
Left Bumper
Left Bumper, Right Bumper & A is to move robot into Substation Pickup (*** robot has to stay close to your alliance zone for auto positioning)
Left Bumper, Right Bumper & X is to stop both platform & Tophat
Left Stick X&Y and Right Stick X is for Platform Navigation Manually
Left Bumper, Right Bumper, Left Trigger, Right Trigger & X is Robot Reset
Left Trigger, Right Trigger & A to put robot Tophat in navigation mode

## Slide 2
+X
-X
+Y
-Y
+X
-X
+Y
-Y
Left Stick
Right Stick
RIGHT
LEFT
UP
DOWN
DPAD
Y
B
A
X
Instructions for Robot Top Hat Driver
Right Trigger
Right Bumper
Left Trigger
Left Bumper
Left Trigger – Move Turn Table Left
Right Trigger – Move Turn Table Right
Left Stick Y – Move Arm Up & Down
Right Stick Y – Move Elbow Up & Down
DPAD UP – Move Wrist Up
DPAD DOWN – Move Wrist Down
DPAD LEFT – Close Claw
DPAD RIGHT – Open Claw
Left Bumper & X is for left ground junction position
Right Bumper & X is for right ground junction position
Left Bumper & A is for left low junction position
Right Bumper & A is for right low junction position
Left Bumper & B is for left medium junction position
Right Bumper & B is for right medium junction position
Left Bumper & Y is for left high junction position
Right Bumper & Y is for right high junction position
Left Bumper, Right Bumper & X is to preset for substation pickup
Left Bumper, Right Bumper & Y is to preset for high junction drop
Left Trigger, Right Trigger & X to substation pickup and ready to drop in any junction
Left Trigger, Right Trigger & Y to drop in high junction from substation continuously